 In address there is space. Endfffffff

That space is register (stored valued or data).

        Register(stores the value) GPIO = 8 change can the bcoz we’re

        0 into 1 in values.

8 Address for one GPIO. Address

To access address or register we are using C.

Register - 8

Register are same but address are different.

* GPIO registers has

        ----------

  (GPIOx_MODER) (MODER,OSPEEDR ... ETC)
        this are short form. Start00000
  (GPIOx_OTYPER)

  (GPIOx_OSPEEDR)

  (GPIOx_PUPDR)

 (GPIOx_IDR)

(GPIOx_ODR)

(GPIOx_BSRR)

 (GPIOx_LCKR)

 (GPIOx_AFRL)

(GPIOx_AFRH)

        -------------

Bose address is register.

For Physical memory for (8 bit) is a bytes.

It is a byte addressable.

(Use decimal)

We can store binary in hexadecimal way.

BcozFor (11 = 1011) we cannot use bcoz it "ll will be confuse so we use hexadecind (0 to 9, A to F
) It'll easy.

Half set find (20 off set 2) 20.2

20+2=22

Module = 22

address = 2.

EG:

[ Bass address =20

address offset=20

Bass + address= 40 ]

If find Bass address easy to find off set, If find off set easy to find Bass address.
Both are some way of process.

Here, For RCC 0X400203800 this is not Bass , 0x40020000 (GPIOA) is Bass.

TO RCC = Bass + RCC off set ->(3800 [that num]).

R = Register

In previous we see that are address.

Now we see Register.

Here, we pointer to access addres to find value.

Volatile we use bcoz don't optimze the given value (or) modizied (convert) the value when we given the INPUT VALUE.

Address Value >Register ( [top] next topic)

 (pervious

      t
opic)

0	0000
1	0001
2	0010
3	0011
4	0100
5	0101
6	0110
7	0111
8	1000
9	1001
A	1010
B	1011
C	1100
D	1101
E	1110
F	1111